Assuming: 1. Graph has been randomly colored as input.
Notation: c(k,v(i)) is the number of edges with color k at node i. d(v) is the degree of node v.R(i) is the traffic from node i.
Rule 1: According to the theorem 10 from the peper, in time slot assignment, each node uses ceil((3R(i)/(2(g-1)))) tunable tranceivers and ceil(W_min) wavelengths.
By using this theorem, we check the sum of c(k,v(i)) for all k and I differ from |V|*ceil((3R(i)/(2(g-1)))) and sort it. Choosing biggest two as next time slot for check.

Pseudo Code:
Check(G)
1	objective=1
2	new_objective=0
3	while objective !=new_objective or not trying all pairs do
4	objective=sum of max(c(k,v(i))for all k) for all I
5	total_tp=|V|*ceil((3d(v(i))/(2(g-1))))
6	for k in g
7	sum=0
8	for all v(i) in |V|
9	sum+=c(k,v(i))
10	diff[k]=sum- total_tp
11	assign g1, g2=index of two biggest element in diff[k] with unmarked color pairs
12	mark these two color-pairs
13	put these 2 colors in new graph, remove other color
14	run algorithm used for g=2
15	put all other edges with colors back
16	new_objective=sum of max(c(k,v(i))for all k) for all I
17	return new_objective

Rule 2:
choose the next two time slots to check based on whether the number of edges in graph with two colors are different lenss than 1
Check(G)
1	objective=1
2	new_objective=0
3	while objective !=new_objective or not trying all pairs do
4	objective=sum of max(c(k,v(i))for all k) for all I
5	for k in g
6	sum=0
7	for all v(i) in |V|
8	sum+=c(k,v(i))
9	A[k]=sum
10	for i,j in g
11	if |A[i]-A[j]|<=1 then
12	color1=i
13	color2=j
14	if color pair i,j unmarked then
15	put these 2 colors in new graph, remove other colors
16	mark this color pair
17	run algorithm used for g=2
18	put all other edges with colors back
19	new_objective=sum of max(c(k,v(i))for all k) for all I
20	else
21	break
22	return new_objective